## Slide 1: Cylindrical orthogonal collision risk management in spacecraft formations
SSDL Lab Meeting
Guggenheim 442
Ulises Núñez (presenter)
15 November 2022

## Slide 2: What is spacecraft formation flying (SFF)?
Definition:
  “A set of more than one spacecraft whose dynamic states are coupled through a common control law”
Implication:
  At least one member of the formation must “track” a desired state relative to another member of the set
Ran et. al (2017)
Notes: Picture SFF [accessed 12 March 2018]:
https://www.sciencedirect.com/science/article/pii/S0094576517301789
SFF:
This work is motivated by interest in realizing sustainable, practical spacecraft formation flight. So I always like to begin these presentations by defining what spacecraft formation flight is.
Read definition of Scharf, Hadaegh and Ploen
Now, that last bit about tracking a relative state with respect to another spacecraft is crucial, because it implies that agents in formation, although physically distinct, are dynamically “joined“. That‘s what makes spacecraft formations a different concept from constellations.
(Side note: The word “connected“ has a graph theoretical meaning, so it is not appropriate. The word “linked“ has a telecommunications meaning, so it is not appropriate. “Coupled“ has other dynamics implications, e.g. Coupled dynamics modes. “Associated“ is too weak. “Related“ is confusing.)

## Slide 3: Spacecraft formation flying (SFF) Examples
Formation keeping (e.g. MMS mission)
Rendezvous & Docking (e.g. with ISS)
NASA (2016)
Schiff et. al. (2011)
Notes: Picture ISS docking [accessed 16 September 2020]:
https://www.nasa.gov/offices/nesc/articles/space-rendezvous
Picture MMS [accessed 16 September 2020]:
https://ntrs.nasa.gov/citations/20180000025
https://www.semanticscholar.org/paper/Monte-Carlo-Simulations-of-the-Formation-Flying-for-Schiff-Dove/192a560326c61a6c11e10d0af1904ea69e70dca6

## Slide 4: Spacecraft formation flying (SFF) NOT Examples
Constellations (e.g. GPS)
Individual spacecraft (e.g. Hubble Space Telescope)
NASA (2020)
GPS.gov (2011)
Notes: Picture HST docking [accessed 16 September 2020]:
https://www.nasa.gov/feature/goddard/2020/hubble-team-wins-2020-michael-collins-trophy
Picture GPS [accessed 16 September 2020]:
https://www.gps.gov/systems/gps/space/

## Slide 5: Spacecraft formation flying (SFF) Benefits
Improved systems engineering attributes (“-ilities”)
Improved system flexibility
  Modularity
  Adaptability
  Maintainability
Improved system robustness
  Fault tolerance
  Reliability
Ran et. al (2017)
Notes: Picture SFF [accessed 12 March 2018]:
https://www.sciencedirect.com/science/article/pii/S0094576517301789

## Slide 6: Spacecraft formation flying (SFF) Benefits (scientific applications)
New Worlds Observer team (2017)
Occultation methods
Notes: Picture NWO/Starshade docking [accessed 16 September 2020]:
https://apps.dtic.mil/dtic/tr/fulltext/u2/a539240.pdf

## Slide 7: Spacecraft formation flying (SFF) Benefits
Synthetic aperture radiometry
Scientific applications
El Maghraby et. al. (2016)
Astrophysics
  Gravitational wave detection
  Exoplanet detection
Earth science
  Weather forecasting
  Climate monitoring
Heliophysics
  High resolution surface imaging
Notes: Picture SAR [accessed 12 March 2018]:
https://eprints.soton.ac.uk/408042/1/IAC_16_B1_2_8_x33950.pdf

## Slide 8: Spacecraft formation flying (SFF) Sources of collision risk
External kinetic threats (i.e. debris)
Internal collision risk
ESA (2019)
Wang et. al. (2018)
Notes: Picture Earth debris environment [accessed 16 September 2020]:
https://www.esa.int/Safety_Security/Space_Debris/Recognising_sustainable_behaviour
Picture relative orbit [accessed 16 September 2020]:
https://www.sciencedirect.com/science/article/pii/S0273117718305696

## Slide 9: Outline
Definition of collision events
Motivating new collision regions
Cylindrical orthogonal collision region
  Norm-ball properties
  Stochastic collision risk feasibility
  Quantitative relationships in stochastic collision risk
Q&A

## Slide 10: Topological notion of collision
a) No-collision condition
b) Collision condition
Notes: Background.Definition of collision
Bear in mind: these balls are surrogates for the size of the object, they are not position pdfs.
Note (11/14/2022): Euclidean balls. Isotropic, and allow for a formulation of collision events that is abstract from relative geometry and relative attitude.

## Slide 11: Obstacle avoidance problem in SFF Contrast vs. standard obstacle avoidance in robotics
Uncluttered environment
Relative orbital dynamics
  Unstable natural modes in any linearization
  Affected strongly by unmodeled forces / model uncertainty
Relative state must be estimated
  Significant estimation errors
Limited onboard resources
  Propellant
  Computing power
Notes: Discussion by Weiss and Dr. Kolmanovsky [weiss2015]
Can’t really be modeled as single integrators; dynamics are rapidly changing in Cartesian space
%as opposed to standard avoidance problem in robotics
Maneuvers constrained by pointing

## Slide 12: Obstacle avoidance problem in SFF Implications
Collision risk must account for relative state uncertainty
  Mitigation in terms of collision risk indicators
  Appropriate choice of risk thresholds
Collision risk must be managed in an ongoing basis
  Quantification for monitoring
  Assessment whether collision risk warrants corrective actions in view of chosen risk thresholds
  If needed, planning and executing maneuvers
Notes: Can’t really be modeled as single integrators; dynamics are rapidly changing in Cartesian space
Collision risk must be managed in an ongoing basis
  Quantification for monitoring
  Assessment whether collision risk warrants corrective actions in view of chosen risk thresholds
  If needed, planning and executing maneuvers

## Slide 13: (Spherical) Collision avoidance constraint satisfaction Computational issues (conceptual)
Mueller et. al. (2013)
NP-Hard
Uncountable constraints
Restrictive assumptions

## Slide 14: (Spherical) Collision avoidance constraint satisfaction Approximations
Approaches
Approximating the same constraint
  Sequential convexification
  Model-predictive control (MPC)
  Artificial potential function
Avoiding a different collision region
  Box-type regions
  2D cylinders
Euclidean vs. Box () ball-collision regions

## Slide 15: Clohessy-Wiltshire (CW) relative orbital dynamics Cross-track plane (radial/cross-track); Sky plane (along-track/cross-track)

## Slide 16: Clohessy-Wiltshire (CW) relative orbital dynamics Cross-plane marginally safe trajectory families

## Slide 17: Clohessy-Wiltshire (CW) relative orbital dynamics In-plane marginally safe trajectory families
Encircling unsafe region
Not encircling unsafe region
Notes: Results.Correlating miss distance and true KPC
Collision risk assessments between true IPC and 99.73% minimum distance (𝝆_𝟑𝝈) are consistent

## Slide 18: Motivation for 3D constraints: Projection IPCs overestimate true IPCs
Every projection IPC is an overestimate of the true IPC
  Applies to any plane choice
If , then the overestimation is strict
  This applies to normally distributed relative positions
Theorem
Núñez Garzón et. al (2022)
Notes: Theory.Projection KPC theory
Explain
Projection pdfs
Projections KPCs
Collision risk as perceived in 2D projections is an overestimate of “true” collision risk as perceived in the full 3D condition. So we definitely want to handle 3D constraints nonconservatively.

## Slide 19: Constructing a cylindrical orthogonal collision region
Balancing concerns in simplifications
  Safety
  Constraint satisfaction tightness
Assumption: 2D solutions are readily available

## Slide 20: Constructing a cylindrical orthogonal collision region
What if we satisfied at least one of these constraints at a time?
  XY plane (in-plane)
  XZ plane (cross-plane)
  YZ plane (sky-plane)
Putting them together
  OR-logic

## Slide 21: Research Questions
#1: what kind of space would we avoid when we do this?
  Is that region well defined?
  What are the properties of those spaces?
  What are the advantages to using this region?
#2: Does it make sense to do collision risk management with it?
  Are stochastic measures of collision risk based on this OR-logic constraint relaxation 1) defined, and 2) computable?
#3: How do collision risk measures based on new region compare to those used in the community?
Notes: How do measures of collision risk compare to other measures (joint-time and instantaneous) that are already used in the community (Euclidean and box-type balls)

## Slide 22: Cylindrical orthogonal norm in Definition
Let in
Cylindrical orthogonal (c.o.) norm
This is a norm in
  Non-negativity
  Homogeneity (or scalar multiplication)
  The Triangle Inequality
  Uniqueness (of the zero vector)

## Slide 23: Cylindrical orthogonal norm in Connection to collision risk management
Construction
Resulting avoided volume

## Slide 24: Cylindrical orthogonal collision region Properties
Cylindrical orthogonal collision region is an open set
It is a measurable set
  Volume is defined
  Probability measures are computable (esp. via pdfs)
It is a convex set (since it’s a ball)
Conservative (but not much) compared to spherical ball
  Volumetrically: +11.9%
  Linearly: +22.5% (worst case)
Comparison to spherical ball

## Slide 25: Cylindrical orthogonal collision region Properties
Deterministic Benefits
Conservative (but not much) compared to spherical ball
  Volumetrically: +11.9%
  Linearly: +22.5% (worst case)
Features:
  Reduced conservatism
  Collision safety is kept
  Easy to compute
What about stochastically?
Comparison to spherical ball

## Slide 26: Probabilistic collision risk indicators Joint-time collision event (JTC)
Notes: JTC: Happens in relative state space: that is, space of relative position and relative velocity. We have to account for how uncertainty evolves over time (changes shape and location) and therefore we need to account for relative velocity also

## Slide 27: Result #1: Joint-time collision risk is *defined*
Assumptions:
  If we define an instantaneous collision condition as an open ball with respect to any 3D vector norm
  If the projection from relative position to relative state space is continuous (and onto)
  If the flow function (that propagates points in relative state space from to ) is continuous
Then:
  The joint-time collision set is open (and hence measurable) in initial relative state space
Consequences:
  Probability of collision is well defined under these assumptions

## Slide 28: Result #2: Joint-time collision risk is “computable”
Assumptions (in addition to 1-3):
  Hard-body radius varies continuously for in
Then:
  Probability of collision can be approximated as a limit of finite timestep approximations
Consequences:
  Probability of collision is practically computable

## Slide 29: Cylindrical orthogonal collision probabilities Bounds
Rationale
Follows from equivalence of finite-dimensional vector norms
Reflect collision set inclusion/exclusion relationships
Bounds (instantaneous + joint-time cases)
Compared norm | Lower bound (multiple of ) | Upper bound (multiple of )
Euclidean () |  | 
Box () |  | 
Compared norm |  | 

## Slide 30: CW Monte Carlo sample distribution (Initial time)
Notes: Theory.Validation
Validate through MC analysis (320 million particles) why so many? Adapting the req of preq = 1E-7

## Slide 31: CW dynamic cases (normal initial state distribution)
Initial state expectations
Cases | With motion | Comments | [deg]
3D.001 | No |  | 0
3D.002 | Yes | and motion in phase | 0
3D. | Yes | and motion out of phase | 15(c 3) ( {0,15, ,345})
Cases |  | Comments | 
3D.001 | No |  | 0
3D.002 | Yes |  | 0
 | Yes |  | 
Initial state covariance
Diagonal
Standard deviation |  |  | 
Relative position (m) | 10 | 5 | 0.5
Rel. position rate (m/s) | 0.25 | 0.75 | 0.05
Standard deviation |  |  | 
Relative position (m) | 10 | 5 | 0.5
Rel. position rate (m/s) | 0.25 | 0.75 | 0.05
Notes: Implementation.CW dynamic cases
Rationale: we are incorporating multiple things here – the indicator definitions + sampling, the probabilistic formulations, + the dynamic models. As this is the beginning of a very long investigation (hopefully), we chose to simplify the relative orbital dynamics involved.

## Slide 32: Computational validation Example 3D.001 (similar for all examples)
Comp. to Euclidean norm ()
Comparison to box norm ()

## Slide 33: Applicability of Results #1, #2
Transfer and Planetary Orbits
Libration point orbits
Swenson (2019)
Parker (2011)

## Slide 34: Applicability of Results #1, #2 to other norms Extrusions of 2D shapes
Polygons (e.g., hexagon)
Extruded circle

## Slide 35: Applicability of Results #1, #2 to other norms Proper 3D shapes
Rectangular cone
Ellipsoid

## Slide 36: Applicability of Results #1, #2 to other norms Truncations of 3D shapes
Truncated rectangular cone
Truncated ellipsoid

## Slide 37: Examples of non-spherical collision regions in the literature
Ellipsoid+ball (does not have norm structure)
Ellipsoid (with norm structure)

## Slide 38: Conclusion
Cylindrical orthogonal collision region
  Motivated
  Definition
  Deterministic properties
  Stochastic collision risk theoretical results
  Stochastic collision risk inequality relationships
  Computational validation

## Slide 39: Questions?