## Slide 1: Implementation of Model Predictive Control for Autonomous Rendezvous and Docking of Small Satellites
SSDL Meeting
Andrew Fear
11/2/21

## Slide 2: Introduction

## Slide 3: Autonomous Rendezvous and Docking
Facilitates creation of larger structures on-orbit
  May be cheaper
  Can replace “pieces” as needed
Autonomy helps alleviate ground resources
  Robust guidance
  Collision detection and avoidance
  Ultimately some decision making
Challenges
  Very Limited Fuel
  Limited Thrust Capabilities

## Slide 4: MPC Background

## Slide 5: Model Predictive Control
Solves the optimal control problem by looking at “cost-to-go” from each state to next and minimizing this cost over some prediction horizon, N.
Typical formulation for predictive control is of the form
Doesn’t make any assumptions about linearity, but doing so can make solving easier
  Incorporates constraints directly into problem to be solved
Solve at each sample time
  Computationally costly
  More robust to disturbances than other guidance (LQR)

## Slide 6: Model Predictive Control

## Slide 7: Dynamics
Classic Clohessy-Wiltshire equations
  Good for close range
  Assumes circular orbits
  x is radial out, y is direction of velocity, z completes right-hand system
In-plane CW equations

## Slide 8: MPC for Autonomous Rendezvous and Docking

## Slide 9: MPC for AR&D
Quadratic Program
  Computationally “simple”
Linear Dynamics (Discretized)

## Slide 10: MPC for AR&D – Objective
Quadratic Cost
  Minimizes actuation effort
  Weights are PSD, Qf is solution to Algebraic Ricatti

## Slide 11: MPC for AR&D - Dynamics

## Slide 12: MPC for AR&D - Dynamics
Discretized CW equations
  Impulse invariant discretization
Assuming impulsive control, instead of a discretization that uses zero-order hold control.

## Slide 13: MPC for AR&D
What if we wanted to ensure docking from a specific direction?
Can use LOS constraint!

## Slide 14: LOS Constraint
Want to stay within a designated cone
Will be added as a penalty in the objective

## Slide 15: MPC for AR&D – With LOS Constraint

## Slide 16: MPC Policy
Some papers use the same MPC formulation for the whole maneuver
  Farther out, cone LOS isn’t important
  As you get closer, need a shorter prediction horizon and can tighten the LOS cone
Split the whole maneuver into three phases
  Far Range (> 2 km)
  Mid Range (10 m – 2 km)
  Close or Final approach (< 10 m)

## Slide 17: Far Range MPC Formulation

## Slide 18: Mid Range MPC Formulation

## Slide 19: Close Range MPC Formulation

## Slide 20: Simulations

## Slide 21: Simulation
Assuming 6DOF thrust for chaser for simplicity
Both MATLAB and 42
  https://github.com/ericstoneking/42
  42 for disturbances and propagating nonlinear EOMs and thruster modeling
Using a convex solver called CVXGEN to solve the MPC optimization at each sample time
  https://cvxgen.com/docs/index.html
  Fast
  C++ and MATLAB
  I’m pushing the limit with the number of variables

## Slide 22: Scenario Parameters
Two CubeSats in LEO
  Assumes 6DOF thruster control (Maximum thrust of 10 N)
  14 kg CubeSats

## Slide 23: MPC Parameters

## Slide 24: Test Scenarios
Case 1: Rendezvous with a V-bar approach
  LOS cone is pointed in the V-bar direction
  Set overshoot constraint to
Case 2: Rendezvous with an R-bar approach
  LOS cone is pointed in the V-bar direction
  Set overshoot constraint to
Case 3: Rendezvous with a tumbling target
  LOS cone rotates with the tumbling target
  Target is tumbling about it’s Earth-pointing axis

## Slide 25: Scenario 1 – V-bar Approach
In-Plane Trajectory
Control Magnitude vs Time

## Slide 26: Scenario 2 – R-bar Approach
In-Plane Trajectory
Control Magnitude vs Time

## Slide 27: Scenario 3 – Tumbling Target
In-Plane Trajectory
Control Magnitude vs Time

## Slide 28: Summary
Ran the MPC policy with changes in formulation (prediction horizon, sampling time, constraints) for 3 scenarios using simulations
  Splitting into phases can cut down on fuel cost, but with longer rendezvous times
  Sim used thruster models to perform the control
MPC policy is able to perform rendezvous with a tumbling target

## Slide 29: Future Work
Use measurement and actuation noise to prove robustness
Run on embedded system hardware to benchmark usability