## Slide 1
SPECTRE: Design of a Dual-Mode Green Monopropellant Propulsion System
AAS Guidance, Navigation and Control Conference February 4, 2022
Brandon J. Colón
Dr. Glenn Lightsey

## Slide 2
Background
SSDL has experience building cold gas and monopropellant propulsion systems
Additive Manufacturing (AM) has enabled the design of volumetrically efficient propulsion systems
Mission | Dry Mass | Total Impulse | Propellant Type
PROX-1 | 6.000 kg | 999 N-s | Cold Gas
BioSentinel | 1.265 kg | 36 N-s | Cold Gas
ASCENT | 3.660 kg | 549 N-s | Cold Gas
LFPS | 5.550 kg | 1800 N-s | Monopropellant
SunRISE | 1.27 kg | 135 N-s | Cold Gas
SWARM-EX | 0.475 kg | 82 N-s | Cold Gas
VISORS | 1.031 – 1.117kg | 117 – 197 N-s | Cold Gas

## Slide 3
What is Dual – Mode?
A Dual – Mode system allows for propulsion technologies to complement each other’s deficiencies
Spectre makes use of both chemical and electrospray propulsion technologies
Partnership between:
  Georgia Tech – SSDL
    System design and integration
    Controller design
  Plasma Processes Inc (PPI)
    Chemical thruster
  MIT – SPL
    Electrospray thrusters
  ESPACE
    Electrospray controller
  NASA – MSFC
    Project Management

## Slide 4
System Specifications
​12U CubeSat
Structure is completely additively manufactured
Both systems are fed from same tank for volume efficiency
  Make use of AF-M315E green monopropellant
 | Chemical | Electrical | Total
ISP (s) | 250 | 1500 | ---
Allocated Propellant (kg) | 4.464 | 0.496 | ---
Delta V (m/s) | 619 | 477 | 1097
Thruster Class (N) | 1 | 2.00E-05 | ---
Prop Flow Rate (g/s) | 0.55 | 5.00E-07 | ---
Number of Thrusters | 1 | 16 | ---
Performance characteristics courtesy of Daniel Cavender

## Slide 5
Proposed ConOps
# | Operation/Sequence | Mission Time
0 | Launch & Deployment | Day 0
1 | Spacecraft Commissioning | Day 0
2 | Prop System Commissioning | Day 1
3 | Chemical Thruster Checkout | Day 1
4 | Electrospray Fill Operation | Day 1
5 | Electrospray Thruster Checkout | Day 1
6 | Chemical Thruster Endurance Burn #1 | Day 2 -3
7 | Electrospray Thruster Endurance Test #1 | Day 4 – 29
8 | Chemical Thruster Endurance Burn #2 | Day 30 -31
9 | Electrospray Thruster Endurance Test #2 | Day 32 – 59
10 | Chemical Thruster Endurance Burn #3 | Day 60 -61
11 | Electrospray Thruster Endurance Burn #3 | Day 62-89
12 | Disposal Burn (Chemical & Electrospray Thrusters) | Day 90
13 | End of Mission | Day 90
Main goal is to demonstrate compatibility and reusability of both systems
  Fill electrospray tanks
  Fire electrospray thrusters
  Fire chemical thruster
  Refill and fire electrospray thrusters

## Slide 6
System Schematic

## Slide 7
System Design – Approach
Mechanical Design
Additively Manufactured Structure – Ti-6Al-4V
226.5mm x 216.5mm x146 mm
Internal Volume: 4.78 L
Dry Mass Estimate: 5.2 kg
Cable Management Bridge
Pump
Isolation Valve
Controller
Electrospray Stands x4
Electrospray Thrusters
x4
Thruster Valve
PT/TC Sensors

## Slide 8
System Design – Integration
Electrospray Thruster Group x4
Chemical Thruster
CPRS Valve x4
Thermal Protection Cone
Controller
Micro Pump
Isolation Valve

## Slide 9
System Design – Tank
Design for Additive Manufacturing
Print along the Z direction
Use necessary internal features as support structures
Route propellant passage lines along the structural features that already need to be printed
Top face open to allow for post machining processes
PMD
PMD
Z
X

## Slide 10
System Design – Tank
Design for Additive Manufacturing
PT/TC interface to read tank properties
PT/TC interface to read passage properties (high pressure)
Thruster valve interface
Thruster interface
1
1
2
4
3

## Slide 11
System Design – Tank
Propellant Management Device (PMD)
  Used to help propellant reach exit port
Make use of Additive Manufacturing
  Printed directly into the main structure
Top View
Cross Section
Z
Y

## Slide 12
System Design – Chemical Thrusters
1N Thruster provided by partners at Plasma Processes Inc (PPI)
Isp:
  250 s – steady state
Estimated Mass: 140 ~ 150 g
Thruster images courtesy of Tomas Hasanof.

## Slide 13
System Design – Electrospray Thrusters
Electrospray thrusters provided by MIT’s Space Propulsion Lab (SPL)
Micromachined emitter tips
Each module consists of 4 thruster heads
Images and electrospray performance characteristics courtesy of Amelia Bruno
 | Per Individual. Thruster Head | Per 4-Thruster Tank/Unit​
Thrust​ | 20 μN​ | 80 μN​
Flow Rate​ | 0.5 μg/s​ | 2 μg/s​
Specific Impulse​ | 1800 s​ | 1800 s​
Dry Mass ​ | -​ | 15 g​
Propellant Volume​ | -​ | 5 mL​

## Slide 14
System Design – Heritage Components
Heritage Components
  Micro-Pump TRL 8
  Micro-Solenoid Valve TRL 8
  Fill/Drain Valve TRL 6
COTS Components
  Solenoid Valves
  Pressure Transducers
  Thermocouples
  Patch Heaters
Micro-solenoid valve
Fill/drain valve
Micropump developed for LFPS

## Slide 15
Future Work
Continue Detailed Design
  Propellant Passage Design
  Weld Plate
Printability Assessment
FlatSat Testing Campaign Demonstrated
  Electrospray remote filling
  Electrospray firing
  Chemical thruster firing
  Final electrospray refill and fire

## Slide 16
Questions?
AAS Guidance, Navigation and Control Conference February 4, 2022
Brandon J. Colón
Dr. Glenn Lightsey