## Slide 1: Multidisciplinary Design Optimization Approach to Integrated Space Mission Planning and Spacecraft Design
Masafumi Isaji, Yuji Takubo, and Koki Ho
Georgia Institute of Technology
Copyright © 2021 by Masafumi Isaji, Yuji Takubo, Koki Ho/Georgia Institute of Technology. Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
www.ascend.events

## Slide 2: Presentation Outline
  Introduction
  Problem Definition
  Proposed Approach
  Case Study: Human Lunar Exploration Campaign
  Conclusion

## Slide 3: Introduction: Integrated Space Mission Planning and Spacecraft Design
  Space Mission Planning and Spacecraft Design should be concurrently optimized
    Space mission planning = Mixed-Integer Quadratic Programming (MIQP) problem
    Spacecraft design = Nonlinear Programming (NLP) problem, no integer variables
    Integrated problem is a Mixed-Integer Nonlinear Programming (MINLP) problem → computationally prohibitive
  Approaches so far:
    Sequential optimization
      i.e., optimize the mission first, then spacecraft
    Piecewise linear approximation of nonlinear portion
      Nonlinearity is not strictly enforced
  Our Approach: Decomposition-Based Optimization

## Slide 4: Integrated MINLP Problem Definition
  → Objective to minimize
  IMLEO in this case
  → Mass Balance Constraint
  → Concurrently Constraint
  → Time Window Constraint
→ SC Design Constraint Only Nonlinear part

## Slide 5: Proposed Approach: Augmented Lagrangian Coordination (ALC)
  ALC is decomposition-based, bi-level formulation with penalty method for MDO [1]:
  Master Problem
    Updates shared variables y/minimizes the sum of penalty functions ϕk
  Subproblem(s)
    Minimizes the local objective fk and local penalty function ϕk
    consistency constraint ck is relaxed and not strictly enforced
yk: local shared variable
zk: local variable
gk: local inequality constraint
hk: local equality constraint
ϕk : penalty function
ck: local consistency constraint
y: shared variable
yk: local shared variable

## Slide 6: Applying ALC to Our Problem
  y includes spacecraft payload capacity, propellant capacity, dry mass (mpv, mfv, mdv)
  Decomposes MINLP into MIQP and NLP subproblems
  Penalty becomes stricter at every outer loop iteration

## Slide 7: Prioritized Shared Variables and New Spacecraft Design Model
  Parametric Spacecraft Sizing
    Subsystem interactions through dry mass
      Dry mass is summation of subsystem mass
      Subsystem mass are function of dry mass
  Prioritized Shared Variables
    some subproblems knows better about some shared variables

## Slide 8: Case Study: Human Lunar Exploration Two-Mission Sequence (Campaign)
  Automatic Initial Guess generation by Mixed-Integer Linear Programming (MILP)
    Piecewise linear (PWL) approximation for nonlinear spacecraft model
    Global optimum with the approx. model
    MILP problems do not need initial guess
    Solutions and comp. time depend on PWL breakpoint increment/number of mesh points
  Results:

## Slide 9: Benchmarking with State-of-the-Art Method
  The embedded optimization method [2]
    A metaheuristics algorithm determines spacecraft parameters
    Send them to space mission planning problem (solved by MILP)
    Three different metaheuristics algorithms are applied:
      Ant Colony Optimization (ACO) [3], Genetic Algorithm (GA) [4], and Particle Swarm Optimization (PSO) [5]

## Slide 10: Visual Comparison of the Two Methods
→ increasing number of generation/mesh points

## Slide 11: Performance Comparison and Conclusion
    Case study (IMLEO minimization problem) best performance comparison
      Proposed method: 676,930kg IMLEO in 16.27s
      Embedded opt. method: 677,221kg IMLEO in 793.9s
    Conclusion
      Proposed method achieves better and consistent solutions in less time due to:
        1. unique problem structure 2. efficient initial guess generation 3. prioritized shared variables 4. specialized solvers for subproblems
      Further room for improvement
        Parallelization of subproblems, MDO problems integration

## Slide 12: References
    [1] Tosserams, S., Etman, L., and Rooda, J., “An augmented Lagrangian decomposition method for quasi-separable problems in MDO,” Structural and Multidisciplinary Optimization, Vol. 34, No. 3, 2007, pp. 211–217. https://doi.org/10.1007/s00158-006-0077-z.
    [2] Taylor, C., “Integrated Transportation System Design Optimization,” Ph.D. thesis, Dept. of Aeronautics and Astronautics, MIT, Cambridge, MA, 2007.
    [3] Schlüter, M., Egea, J. A., and Banga, J. R., “Extended ant colony optimization for non-convex mixed integer nonlinear programming,” Computers & Operations Research, Vol. 36, No. 7, 2009, pp. 2217–2229. https://doi.org/https://doi.org/10.1016/j.cor.2008.08.015.
    [4] Holland, J. H., “Genetic Algorithms,” Scientific American, Vol. 267, No. 1, 1992, pp. 66–73. URL http://www.jstor.org/stable/24939139.
    [5] Kennedy, J., and Eberhart, R., “Particle swarm optimization,” Proceedings of ICNN’95 - International Conference on Neural Networks, Vol. 4, 1995, pp. 1942–1948 vol.4. https://doi.org/10.1109/ICNN.1995.488968.16

## Slide 13
Thank You
Any Questions?
Preprint available on arXiv and ResearchGate

## Slide 14
www.ascend.events
Powered by